### THE WEST COAST REGIONAL COUNCIL

WANGANUI RIVER  RATING DISTRICT

ASSET MANAGEMENT PLAN

October 2014

CONTENTS

EXECUTIVE SUMMARY………………………………………………………………………………………………………….3

SECTION 1: INTRODUCTION…………………………………………………………………………………………………4

SECTION 2: SERVICE LEVELS………………………………………………………………………………………………..7

SECTION 3: FUNDING…………………………………………………………………………………………………………10

SECTION 4: PERFORMANCE MEASURES………………………………………………………………………………..11

APPENDIX 1: EXPENDITURE SINCE 1993……………………………………………………………………..……….12

APPENDIX II – ASSET REGISTER AND INFRASTRUCTURE MAPS	13

# EXECUTIVE SUMMARY

Under the Local Government  Act 2002 Councils are required to develop ‘Asset Management Plans’ to demonstrate that they are managing the infrastructure for which they have responsibility.

This plan sets out the history of the scheme so there is a record of the major decisions, including expenditure. It identifies the Objective(s) of the scheme as well as the methods of monitoring the condition of the assets, and determining the annual maintenance needed to retain the service level.

The Wanganui River Maintenance Scheme extends from the State Highway Bridge downstream for 13 kilometres. The area protected is predominantly dairy farming with some dry-stock properties. Community infrastructure such as roads, power and telephone lines all derive benefit from the river control system.

The plan also includes the Infrastructural Asset Register which details all of the Scheme’s assets and their latest valuation.

Maintenance Expenditure vs Capital Expenditure

The aim of maintenance is to ensure the infrastructure assets are kept at a standard where they can always perform to their service level. Where rock is required to be placed on an existing stopbank under direct attack from the river, the protection required to maintain the existing stopbank at its same service potential would be charged to the scheme maintenance account.

Capital works are generally defined as works which increase the service level of the scheme.  Such work would include increasing the design standard or the area covered by a scheme and works to increase security or performance of an erosion control system or structure over and above that identified in the asset plan.

# SECTION 1: INTRODUCTION

1.1	PURPOSE OF AN ASSET MANAGEMENT PLAN

This Asset Management Plan defines the objectives and performance standards of the Wanganui Rating District scheme for which the Regional Council has the maintenance responsibility. It also provides a basis upon which the effectiveness of maintenance performance can be measured.

This asset management plan:

- Identifies the service level for the Rating District.

- Describes the history of the rating district and identifies it’s assets.

- Describes the methods used to maintain the service level of these assets.

- Complies with the regulatory requirements of the Local Government Act 2002.

# 1.2	BACKGROUND

Wanganui River – Left Bank

Severe flooding of the Hari Hari Flat during the early part of 1913 resulted in the first protection works being carried out on the Wanganui River. A stopbank with wire gabion basket protection was constructed from a point on the hill 200 metres west of the old main road bridge abutment and extended downstream for 400 metres to prevent further flood overflows from causing damage to developed farmland downstream.

There is no record of any further work being carried out until 1958 when Mr. V. Berry constructed a low stopbank on his frontage approximately 8 kilometres below the state highway bridge to prevent overflows from the river ruining his pasture.

In 1960 approximately 5 kilometres below the state highway bridge on Ford Brothers frontage a boulder gabion stronghead was constructed and a stopbank extended upstream for 750 metres to prevent flooding of their property.

In 1962 the Hari Hari Flat Protection Scheme which involved the construction of 4.4 kilometres of stopbanking and 18,000 tonnes of rock protection was approved by Soil Conservation and Rivers Control Council.  The estimated cost of the scheme was 36,000 Pounds.  A loan of 9,000 Pounds to finance the local share of the scheme work was granted in July 1963. A special rate to pay back the loan and maintain the scheme works was adopted in May 1964.

The new stopbank extended downstream from the old bank completed in 1913 for 4.4 kilometres and involved 52,000 cubic metres of earthworks. Rock protection for this bank was carried out during 1965 and involved approximately 18,000 tonnes of rock placed in various protection works.

The access road up to the Wanganui Quarry was completed during the contract for the acquisition of rock for the scheme.

Approximately 9.5 kilometres below the state highway bridge on Mr V. Berry’s frontage a hook groyne and 2.3 kilometres of stopbanking was constructed during 1966.  This work was subsidised but was not part of the scheme works at that time.

2.5 kilometres below the state highway bridge 650 metres of stopbanking, hook groyne and training wall was constructed in 1972 to prevent erosion to the main scheme stopbank. 700 metres below the Wanganui Flat road a stopbank, hook groyne and training wall extending downstream for 1.7 kilometres was constructed in 1974 for the La Fontaine Farm Settlement and others. A stopbank 2.5 kilometres in length connecting V. Berry’s bank and the La Fontaine Farm Settlement bank was completed in 1975.

In January 1982, 1.8 kilometres below Ford Brothers stronghead, 200 metres of stopbanking was washed out and was replaced by a hook groyne and training wall.  The stronghead of this hook groyne was destroyed by a flood in January 1994.

A stopbank 1.6 kilometres in length connecting Ford Brothers stopbank and V. Berry’s stopbank was completed in 1982.

600 metres below the state highway bridge a rock retard was constructed in 1984 to provide protection to the main stopbank.

Wanganui River - Right Bank

In 1966 severe erosion on the right bank 2 kilometres below the state highway bridge resulted in 5,000 tonnes of rock being placed on the McGrath frontage. Below the confluence of Evan’s Creek a 100 metre hook groyne with rock protection was constructed in 1969. A rock training wall extending approximately 1 kilometre downstream from the end of the hook groyne was constructed in 1971 and a rail groyne extending a further 700 metres downstream was constructed in 1972. A second hook groyne and stopbank extending downstream for 1.1 kilometres from the one built in 1969 was constructed in 1974.

2.5 kilometres below the state highway bridge a hook groyne and training wall 500 metres in length was completed in 1976.  Flooding during 1980 washed the riverbank out on the inside of the hook groyne and a second hook groyne was constructed in 1981.  The hook groyne and training wall completed in 1976 was destroyed by flooding during 1985 and replaced by a stopbank.

1.5 kilometres below the state highway bridge on McGrath’s frontage a stopbank 240 metres in length with rock protection was completed in 1987.

A revised classification to finance maintenance work in part of the Poerua Valley, Wanganui River, La Fontaine, Hari Hari township and lower La Fontaine drainage schemes was adopted by the Westland Catchment Board in May 1985.

The classification was further revised with the Poerua Valley taken out of the area.  This classification was adopted by the Regional Council in April 1993

Drainage

At the request of the Hari Hari branch of Federated Farmers, an economic assessment of potential areas for development in the Poerua Valley, Evans Creek and Hari Hari areas was carried out by farm management research officers of the Department of Agriculture.

As a result of the assessment the Westland Catchment Board prepared a drainage scheme for the La Fontaine Stream catchment.

The scheme included the reconstruction of La Fontaine Stream and major tributaries as well as internal farm drainage.  The estimated cost of the scheme was 9225 Pounds. This scheme was approved by Soil Conservation and Rivers Control Council in November 1959.

The classification for the La Fontaine Drainage Scheme was adopted in April 1961 by the Westland Catchment Board. In 1966 the drainage scheme was extended up to Robertson’s Road and including land adjacent to the state highway and the Hari Hari Township. This area was classified as the Hari Hari Township Drainage Scheme.

A revised classification to finance maintenance work in part of the Poerua Valley, Wanganui River, La Fontaine, Hari Hari Township and Lower La Fontaine Drainage Schemes was adopted in May 1985.

The classification was further revised with the Poerua taken out of the area. This classification was adopted by the Regional Council in April 1993.

1.3 	DESCRIPTION OF ASSETS

The Rating District assets consist of all those works outlined in the Infrastructural Asset Register. The total replacement value of these works was $14.9M as at June 2014.

The capital value of land and buildings within the confines of the scheme is $78,573,100.

| Asset Class | Value |
| --- | --- |
| Rock | $8,128,920 |
| Rock (Stockpiled) | $217,471 |
| Fill | $4,580,438 |
| Structures | $10,000 |
| Rubble | $36,000 |
| Excavation | $275,160 |
| Cleanout | $82,320 |
| Contingency and Administration | 1,626,297 |
| TOTAL | $14,956,606 |

Note that a 10% contingency to cover design and a 2% estimate for administration of the work including resource consent costs has been added to more fairly indicate total replacement costs.

1.4	MAINTENANCE EXPENDITURE

Appendix I shows expenditure since 1993. The average annual expenditure is $110,045

# SECTION 2: SERVICE LEVELS

2.1	OBJECTIVES

The objectives of the Wanganui Rating District are:

- To reduce bank erosion and flooding on the existing structures between the State Highway Bridge and the end of the stopbank 13 kilometres downstream.

- To maintain existing creeks and drains included in the La Fontaine and Lower La Fontaine and Hari Hari Township Drainage Schemes to their original plan specifications.

The historic "Existing Standard" was 900mm above the highest known flood. The Council has suggested that an analysis be commissioned to quantify the actual level of protection that the scheme currently provides. However, the rating district has decided that they do not wish to have any new analysis undertaken. Given that there has been no analysis carried out the scheme structures will continue to be maintained to the dimensions that they were originally constructed.

2.2	MAINTENANCE PROGRAMME

An annual maintenance programme is prepared each year in consultation with the Wanganui ratepayers prior to adoption by the Council for inclusion in the Annual Plan.

In preparing the annual maintenance programme consideration will be given to:

- An inspection to identify works requiring immediate repair.

- works anticipated as being required given a ‘normal’ season.

- flexibility to meet unbudgeted damages.

An annual report will outline the condition of the scheme assets and maintenance works and expenditure required for the coming financial year.

Stopbanks

Stopbanks are man made structures generally running parallel to the flow of the river that are built to raise the bank level and hence increase the capacity of the river. They are usually constructed of compacted river gravels with a grass cover and do not have the strength to resist the erosive forces of a river in flood without adequate bank protection works in place.

Maintenance includes repair of any scouring, vegetation removal to facilitate access, control of stock to prevent damage to stopbank batter slopes, topping up of stopbanks as required to maintain stopbank capacity in terms of design.

Stopbanks can potentially be damaged by:

- Failure of a training groyne such as a rock retard which can allow the full force of the river to suddenly run along a relatively unprotected stopbank, and cause scouring of stopbanks in excess of 50 metres in length

- Overtopping: Stopbanks are generally not designed to sustain overtopping. They may however be capable of sustaining minor overtopping for a short duration in flows not exceeding 100mm in depth over the top of the bank. Overtopping of durations greater than an hour may scour the back batter resulting in failure of the structure, it is therefore important to ensure there is an even and strong vegetation cover on the landward batter.

- Piping: Flow through porous bank or foundation material can wash out fines leading to a collapse.

- Stock and Vehicles: Can remove cover and wear ruts in surface resulting in weakness.

- Construction: Construction of pipelines cables under stopbanks as well as holes on top of stopbanks can weaken the structure. Drainage channels should not be located at the toe of stopbanks.

- Earthquake: Stopbanks can be damaged in the event of an earthquake by cracking vertical or horizontal displacement, or by liquefaction of the foundation material.

Erosion Control / River Training

Erosion control works consist of rock placed in continuous riprap, spur groynes, stub groynes, strongheads, hook groynes, and in river training retards. They are built to provide protection to stopbanks from the river’s erosive forces during floods, by training the river into a stable pattern, or to reduce velocities along stopbanks by using stub rock groynes.

Only limited river training is carried out by way of channel improvements by diversion or extraction of river gravels. This is generally accepted as only having a limited and temporary influence on the channel hydraulics (performance).

Erosion control structures are constructed to absorb the energy of the river, to control the alignment of the flow of the rivers, and subsequently give the required protection to stopbanks and natural banks. Because of this they are the areas with the major exposure to damage. 	The meander of a river can change significantly by floods of only moderate duration.  This can result in an acute angle of attack of protection structures resulting in damage which is disproportional to the flood discharge. Likewise erosion control works already weakened from previous floods may sustain damage disproportionate to the flood discharge.

It is very important to ensure damage to bank protection structures is undertaken swiftly and to ensure:

- Rock training walls are kept to the required height to lessen failure.

- Any slumping of rock off strongpoints, spur groynes and rip rap are topped up.

- Rock is of a durable nature, angular and of the correct grading size.

Drainage and Creek Channels

Drains and Creeks are used to discharge runoff water from land to river systems. Drains are man made structures usually created to improve land use. Creeks, which are natural channels are used in a similar manner. To maintain a drain’s channel capacity it is essential to:

- Keep drains and channels clear of siltation, weed and vegetation growth

- Control stock around the banks and repair any stock damage to banks and batters.

2.3	DAMAGE EXPOSURE

River control works are constructed in a very high energy environment with the purpose of resisting and absorbing some of that energy.  It is considered that no matter what the standard of maintenance carried, it is inevitable that damage will occur to structures.

An assessment of maximum damage potential was derived from estimating the damage ratios and costs for three flood events and is in vicinity of $2,300,000.

| FLOOD EVENT SIZE | VALUE | DAMAGE RATIO | DAMAGE EXPOSURE |
| --- | --- | --- | --- |
| 20 Year | $14,956,606 | 10% | $1,495,660 |
| 100 Year | $14,956,606 | 20% | $2,991,321 |
| 500 Year | $14,956,606 | 20% | $2,991,321 |

# SECTION 3: FUNDING

3.1	MAINTENANCE

Maintenance is funded by targeted rates, the level of rating being determined each year in the Annual Plan process following:

- Preparation of an annual works programme and corresponding budget.

- Consultation with Rating District.

- Adoption of draft programme and budget by Council.

- Adoption of final Annual Plan by Council.

3.2	DAMAGE REPAIRS

Routine damage repairs are funded by a combination of:

- carrying out work as scheduled in annual works programme.

- reprioritising works identified in the annual works programme.

- use of financial reserves.

Major damage repairs would be funded by loans raised by the Council and repaid by targeted rating over a number of years.

3.3	FINANCIAL RESERVES

Financial reserves are held within each rating districts account to provide the following.

- meet the costs of unscheduled works.

- enable an immediate response to flood damage repairs.

- prevent major fluctuation in rating levels annually.

The level of financial reserves held in each rating account is determined by the assessment of risk damage and the need for unprogrammed works.

3.4	DEPRECIATION

Rating District schemes are designed to be maintained in perpetuity by constantly repairing and replacing component parts which are damaged by the constant wear and tear. Because there is a constant cycle of replacement of elements of the infrastructure, depreciation of the value of the assets is not appropriate and funding of depreciation is not necessary. This approach is consistent with the NZ Infrastructure Asset Valuation and Depreciation Guidelines (Section 5.4.4).

3.5	MAINTENANCE VS CAPITAL EXPENDITURE

The aim of maintenance is to ensure the infrastructure assets are kept at a standard where they can always perform to their service level. Where rock is required to be placed on an existing stopbank under direct attack from the river, the protection required to maintain the existing stopbank at its same service potential would be charged to the scheme maintenance account.

Capital works are generally defined as works which increase the service level of the scheme.  Such work would include increasing the design standard or the area covered by a scheme and works to increase security or performance of an erosion control system or structure over and above that identified in the asset plan.

# SECTION 4: PERFORMANCE MEASURES

The overall performance measure is that the infrastructure assets are maintained to meet their service levels at all times.

The following procedures will be adopted to ensure the adequacy of maintenance.

Annually

- Produce annual works report for the rating district to include type of work to be undertaken, quantities, location and costs.

- Organise contracts for agreed scheme work, oversee contract completion and report to Council.

(iii)	Report on works undertaken during the previous financial period to the rating district ratepayers and Council.

Performance Measure

No reports of stopbanks or erosion protection works requiring repairs without an agreed programme of remedial work in progress.

Triennially

(i)	Re-fly aerial photographs of the area, analysing these photographs to assess changes in river meander patterns that could impact on Rating District Assets.

(ii)	Re-measure cross section river profiles to determine whether the riverbed is stable, or aggrading, and to identify management issues or options.

(iii)	Revaluation of the asset schedule to include any additional rock placed on stopbanks and bank protection works over the three year period.

(iv)	Review this Asset Management Plan

Performance Measure

Report to Council and ratepayers on revaluation of assets and the Plan review.

# APPENDIX 1:	EXPENDITURE SINCE 1993

| 1993 | 1994 | 1995 | 1996 | 1997 | 1998 | 1999 | 2000 |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 127,319 | 161,935 | 55,452 | 181,419 | 69,531 | 61,952 | 67,204 | 28,380 |
| 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 |
| 3,799 | 53,197 | 23,317 | 12,865 | 12,449 | 136,043 | 118,914 | 130,313 |
| 2009 | 2010 | 2011 | 2012 | 2013 | 2014 |  |  |
| 203,221 | 197,696 | 271,653 | 104,539 | 107,294 | 292,499 |  |  |

| Total Expenditure | $ 2,420,991 |
| --- | --- |
| Average Expenditure | $ 110,045 |
| Average Expenditure as a % of Asset Value | 0.74% |

As at 30 June 2014, the value of the Wanganui Rating District Scheme assets is $14,956,606.

APPENDIX II – ASSET REGISTER AND INFRASTRUCTURE MAPS

|  |  | WANGANUI RATING DISTRICT |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  | Infrastructural Assets - Amended to 24 March 2015 |  |  |  |  |  |  |  |
|  |  | Refer to Plan No. S 897/52 Sheets 1-6 |  |  |  |  |  |  |  |
|  |  |  | Rock | Stockpile | Fill | Structures | Rubble | Excavation | Cleanout |
|  |  |  | tonne |  | m³ | dollar | tonne | drains m³ | Metres |
|  |  | LEFT BANK |  |  |  |  |  |  |  |
| 1 |  | Rock Retard |  |  |  |  |  |  |  |
|  |  | 250 lineal metres | 7050 |  |  |  |  |  |  |
|  |  | added 1997/98 | 200 |  |  |  |  |  |  |
|  |  | added 1998/1999 | 1000 |  |  |  |  |  |  |
| 2 |  | Rock Retard - 150 lineal metres | 6000 |  |  |  |  |  |  |
|  |  | added 1997/98 | 500 |  |  |  |  |  |  |
|  |  | added 1999/2000 | 400 |  |  |  |  |  |  |
|  |  | Added October 2002 | 200 |  |  |  |  |  |  |
| 3 |  | Rock Spur Groyne | 300 |  |  |  |  |  |  |
| 4 |  | Rock Spur Groyne | 300 |  |  |  |  |  |  |
| 5 |  | Rock rip rap - 90 lineal metres |  |  |  |  |  |  |  |
|  |  | Rock protection on stronghead of |  |  |  |  |  |  |  |
|  |  | hook groyne | 3500 |  |  |  |  |  |  |
| 6 |  | Rock stockpile |  | 500 |  |  |  |  |  |
| 7 |  | Rock Spur Groyne | 100 |  |  |  |  |  |  |
| 8 |  | Rock Spur Groyne | 100 |  |  |  |  |  |  |
| 9 |  | Rock stockpile on edge of stockbank |  | 50 |  |  |  |  |  |
| 10 |  | Rock rip rap - 30 lineal metres | 150 |  |  |  |  |  |  |
| 11 |  | Rock rip rap - 100 lineal metres | 1000 |  |  |  |  |  |  |
| 12 |  | Rock protection on stronghead of |  |  |  |  |  |  |  |
|  |  | hook groyne | 3000 |  |  |  |  |  |  |
| 13 |  | Main Stopbank |  |  |  |  |  |  |  |
|  |  | Point A-B |  |  |  |  |  |  |  |
|  |  | 2400 lineal metres. Average height |  |  |  |  |  |  |  |
|  |  | 3.5 metres, 4 metre topwidth, |  |  |  |  |  |  |  |
|  |  | 2:1 batters |  |  | 92400 |  |  |  |  |
| 13 | a | Rock stockpile |  | 500 |  |  |  |  |  |
|  |  | taken 1997/98 |  | -500 |  |  |  |  |  |
|  |  | added 1998/1999 |  | 350 |  |  |  |  |  |
|  |  | taken 1998/1999 |  | -84 |  |  |  |  |  |
|  |  | added 1999/2000 |  | 150 |  |  |  |  |  |
|  |  | Deducted February 2004 to #33 |  | -80 |  |  |  |  |  |
|  |  | Added April 2006 |  | 300 |  |  |  |  |  |
|  |  | Deducted November 2006 (To #40) |  | -60 |  |  |  |  |  |
|  |  | Deducted December 2006 (To #41) |  | -200 |  |  |  |  |  |
|  |  | Added December 2006 |  | 344 |  |  |  |  |  |
|  |  | Added May 2007 |  | 100 |  |  |  |  |  |
|  |  | Added July 2008 - Contract R 2008 / 4 |  | 1,000 |  |  |  |  |  |
|  |  | Deducted December 2009 to # 21 - Henry Adams |  | -612 |  |  |  |  |  |
|  |  | Added December 2009 ex Quarry - Henry Adams |  | 612 |  |  |  |  |  |
|  |  | Deducted December 2009 to #21 - Arnold Contracting |  | -700 |  |  |  |  |  |
|  |  | Deducted January 2010 to #21 - Arnold Contracting |  | -450 |  |  |  |  |  |
|  |  | Deducted January 2010 to #21 - Arnold Contracting |  | -250 |  |  |  |  |  |
|  |  | Adde jan 2010 - Arnold - Contract R 2010.3 |  | 1,900 |  |  |  |  |  |
|  |  | Deducted Set 2012 - Arnold to # 25 - Arnold |  | -748 |  |  |  |  |  |
|  |  | Added November 2012 -MBD ex ianthe - MBD |  | 798 |  |  |  |  |  |
| 14 |  | Main Stopbank |  |  |  |  |  |  |  |
|  |  | Point B-C |  |  |  |  |  |  |  |
|  |  | Main sstopbank - 1350 lineal metres |  |  |  |  |  |  |  |
|  |  | 4 metre topwidth, average height 3m |  |  |  |  |  |  |  |
|  |  | 2:1 batters |  |  | 40500 |  |  |  |  |
|  |  | added 1999/2000 |  |  | 200 |  |  |  |  |
|  |  | added December 2000 |  |  | 5000 |  |  |  |  |
| 15 |  | Rock Stockpile |  | 0 |  |  |  |  |  |
|  |  | Added May 2007 |  | 200 |  |  |  |  |  |
|  |  | Deducted December 2009 to # 12 - Henry Adams |  | -200 |  |  |  |  |  |
|  |  | Added December 2009 ex Quarry - Henry Adams |  | 162 |  |  |  |  |  |
|  |  | Deducted Jan 2010 to # 21 - Arnold |  | -162 |  |  |  |  |  |
|  |  | Added Jan 2010 - Contract R 2010.3 - Arnold |  | 91 |  |  |  |  |  |
| 16 |  | Rock retard | 3680 |  |  |  |  |  |  |
|  |  | added 1997/98 | 300 |  |  |  |  |  |  |
|  |  | added 1997/1998 | 40 |  |  |  |  |  |  |
|  |  | added 1998/1999 | 84 |  |  |  |  |  |  |
|  |  | added 1999/2000 | 80 |  |  |  |  |  |  |
|  |  | Added May 2007 | 300 |  |  |  |  |  |  |
|  |  | Added September 2011 - Arnold (ex McGrath's) | 228 |  |  |  |  |  |  |
| 16 | a | Rock Spur | 125 |  |  |  |  |  |  |
| 16 | b | Rock Spur | 125 |  |  |  |  |  |  |
| 16 | c | Rock Spur | 125 |  |  |  |  |  |  |
| 16 | d | Rock Spur | 125 |  |  |  |  |  |  |
| 17 |  | 3 rock spur groynes | 1000 |  |  |  |  |  |  |
|  |  | added 1998/1999 | 100 |  |  |  |  |  |  |
|  |  | added 1999/2000 | 170 |  |  |  |  |  |  |
| 18 |  | Rock rip rap - 55 lineal metres | 550 |  |  |  |  |  |  |
|  |  | Added December 2013 | 216 |  |  |  |  |  |  |
| 18 | a | Rock Spur Groyne | 350 |  |  |  |  |  |  |
|  |  | Added October 2002 | 100 |  |  |  |  |  |  |
|  |  | Added May 2007 | 200 |  |  |  |  |  |  |
|  |  | Added April 2006 | 200 |  |  |  |  |  |  |
|  |  | Topup added January 2013 | 50 |  |  |  |  |  |  |
| 19 |  | Rock protection on stronghead | 1000 |  |  |  |  |  |  |
|  |  | added 1997/98 | 540 |  |  |  |  |  |  |
|  |  | added 1999/2000 | 150 |  |  |  |  |  |  |
|  |  | Added May 2007 | 200 |  |  |  |  |  |  |
|  |  | Added 31 October 2007 | 64 |  |  |  |  |  |  |
|  |  | Added November 2008 Contract R 2008 / 11 | 40 |  |  |  |  |  |  |
|  |  | Added Sept 09 - Contract R 2009/12 - MBD | 18 |  |  |  |  |  |  |
|  |  | Added jann 2010 ex S/P #13a | 50 |  |  |  |  |  |  |
|  |  | Added May 2014 - Topup over 40m | 1116 |  |  |  |  |  |  |
| 19 | a | 3 rock spurs added 1997/98 | 200 |  |  |  |  |  |  |
|  |  | Added October 2002 | 100 |  |  |  |  |  |  |
| 19 | b | 2 rock spurs added 1997/98 | 100 |  |  |  |  |  |  |
| 20 |  | Rock Spur Groyne | 50 |  |  |  |  |  |  |
| 20 | a | added 1997/98 | 300 |  |  |  |  |  |  |
| 21 | * | Rock Spur Groyne (Destroyed December 2009) | 250 |  |  |  |  |  |  |
|  |  | added 1999/2000 (Destroyed December 2009) | 50 |  |  |  |  |  |  |
|  |  | New riprap #21 added December 2009 - Henry Adams |  |  |  |  |  |  |  |
|  |  | Added December 2009 ex S/P # 55 - Henry Adams | 54 |  |  |  |  |  |  |
|  |  | Added December 2009 ex S/P # 31a - Henry Adams | 140 |  |  |  |  |  |  |
|  |  | Added December 2009 ex S/P # 15 - Henry Adams | 200 |  |  |  |  |  |  |
|  |  | Added December 2009 ex S/P # 13a - Henry Adams | 612 |  |  |  |  |  |  |
|  |  | Added December 2009 ex Quarry - Henry Adams | 738 |  |  |  |  |  |  |
|  |  | Added December 2009 ex Quarry - Henry Adams | 378 |  |  |  |  |  |  |
|  |  | Added December 2009 ex 13a - Arnold Contracting | 700 |  |  |  |  |  |  |
|  |  | Added January 2010 ex #13a - Arnold | 650 |  |  |  |  |  |  |
|  |  | Added Sept 2010 - R 2010.16 - Arnold | 40 |  |  |  |  |  |  |
| 22 | * | Rock Spur Groyne (Destroyed December 2009) | 100 |  |  |  |  |  |  |
|  |  | Added May 2007 | 60 |  |  |  |  |  |  |
|  |  | Added July 2008 - Contract R 2008 / 4 | 100 |  |  |  |  |  |  |
| 22 | a | Riprap added September 2011 - Arnold (Ex McGrath's) | 300 |  |  |  |  |  |  |
|  |  | Added December 2013 | 1710 |  |  |  |  |  |  |
| 23 | * | 12 rock spur groynes (Destroyed December 2009) | 2524 |  |  |  |  |  |  |
|  |  | added 1997/98 | 200 |  |  |  |  |  |  |
|  |  | added 1997/1998 | 150 |  |  |  |  |  |  |
| 23 | b | Riprap added September 2011 - Arnold (Ex McGrath's) | 276 |  |  |  |  |  |  |
| 24 | * | 4 concrete and rock spur groynes(Destoyed Dec 2009) | 900 |  |  |  |  |  |  |
|  |  | added 1997/98 | 150 |  |  |  |  |  |  |
|  |  | added 1999/2000 | 50 |  |  |  |  |  |  |
| 25 |  | Rock Protection on Stronghead of |  |  |  |  |  |  |  |
|  |  | hook groyne (Vic's Hook) | 10000 |  |  |  |  |  |  |
|  |  | added 1997/98 | 100 |  |  |  |  |  |  |
|  |  | added 1999/2000 | 50 |  |  |  |  |  |  |
|  |  | Added October 2002 | 60 |  |  |  |  |  |  |
|  |  | Added July 2003 | 100 |  |  |  |  |  |  |
|  |  | Added April 2006 | 100 |  |  |  |  |  |  |
|  |  | Added May 2007 | 100 |  |  |  |  |  |  |
|  |  | Added Sept 2009 Contract R 2009/12 - MBD | 200 |  |  |  |  |  |  |
|  |  | Added September 2012-Arnold (Ex S/P #13a) | 748 |  |  |  |  |  |  |
| 26 |  | Main stopbank - Point C-D |  |  |  |  |  |  |  |
|  |  | 450 lineal metres |  |  |  |  |  |  |  |
|  |  | Average height 3.5 metres |  |  |  |  |  |  |  |
|  |  | 4 metre topwidth 2:1 batter |  |  | 17500 |  |  |  |  |
| 27 |  | Rock rip rap |  |  |  |  |  |  |  |
|  |  | 450 lineal metres at 15/tonne metre | 6750 |  |  |  |  |  |  |
|  |  | Added October 2002 | 40 |  |  |  |  |  |  |
|  |  | Added July 2003 | 150 |  |  |  |  |  |  |
|  |  | Added February 2004 ex S/P #38 | 40 |  |  |  |  |  |  |
| 28 |  | Earth Spur Stopbank |  |  |  |  |  |  |  |
|  |  | 15 lineal metres, 4 metre topwidth |  |  |  |  |  |  |  |
|  |  | 1.5:1 batters. Average height 4.0 metres |  |  | 600 |  |  |  |  |
|  |  | Added July 2003 | 100 |  |  |  |  |  |  |
| 29 |  | Rock Protection on earth spur |  |  |  |  |  |  |  |
|  |  | stopbank | 1200 |  |  |  |  |  |  |
| 30 |  | Main Stopbank Point D-E |  |  |  |  |  |  |  |
|  |  | 800 lineal metres |  |  |  |  |  |  |  |
|  |  | Average height 4 metres |  |  |  |  |  |  |  |
|  |  | 2:1 batters, 4 metres topwidth |  |  | 38500 |  |  |  |  |
| 30 | a | Rock rip rap - 200 lineal metres | 1400 |  |  |  |  |  |  |
|  |  | Deducted November 2006 |  |  |  |  |  |  |  |
| 31 |  | Spur Stopbank |  |  |  |  |  |  |  |
|  |  | 80 lineal metres, 4 metres topwidth |  |  |  |  |  |  |  |
|  |  | 1.5:1 batters, average height 3 metres |  |  | 2050 |  |  |  |  |
|  |  | Added April 2006 | 100 |  |  |  |  |  |  |
| 31 | a | Stockpile |  |  |  |  |  |  |  |
|  |  | Added December 2006 |  | 140 |  |  |  |  |  |
|  |  | Deducted May 2007 |  | -100 |  |  |  |  |  |
|  |  | Added May 2007 |  | 100 |  |  |  |  |  |
|  |  | Deducted December 2009 to # 21 - Henry Adams |  | -140 |  |  |  |  |  |
|  |  | Added Sept 2010 - R 2010.16 - Arnold |  | 140 |  |  |  |  |  |
| 32 |  | 90 lineal metres rock rip rap |  |  |  |  |  |  |  |
|  |  | 25 tonnes per metre | 2250 |  |  |  |  |  |  |
|  |  | Added October 2002 | 380 |  |  |  |  |  |  |
|  |  | Added from #31a May 2007 | 100 |  |  |  |  |  |  |
| 33 |  | 620 lineal metres rock rip rap |  |  |  |  |  |  |  |
|  |  | 10 tonne/metre | 6200 |  |  |  |  |  |  |
|  |  | added 1997/98 | 70 |  |  |  |  |  |  |
|  |  | added 1998/1999 | 250 |  |  |  |  |  |  |
|  |  | added 1998/1999 | 50 |  |  |  |  |  |  |
|  |  | Added July 2003 | 40 |  |  |  |  |  |  |
|  |  | Added January 2004 ex Stockpile 38 | 100 |  |  |  |  |  |  |
|  |  | Added February 2004 ex S/P 13a | 80 |  |  |  |  |  |  |
|  |  | Added February 2004 ex S/P 38 | 100 |  |  |  |  |  |  |
| 34 |  | Main Stopbank Point E-F |  |  |  |  |  |  |  |
|  |  | 1000 lineal metres |  |  |  |  |  |  |  |
|  |  | of stopbank, average height |  |  |  |  |  |  |  |
|  |  | 3 metres. 4 metres topwidth |  |  | 30000 |  |  |  |  |
|  |  | added 1997/98 |  |  | 3800 |  |  |  |  |
|  |  | Added February 2014 | 200 |  |  |  |  |  |  |
| 35 |  | Rock rip rap - 30 lineal metres | 150 |  |  |  |  |  |  |
| 35 | a | Rock rip rap - 20 lineal metres added | 300 |  |  |  |  |  |  |
|  |  | added 1999/2000 | 100 |  |  |  |  |  |  |
| 36 |  | Rock rip rap - 20 lineal metres | 200 |  |  |  |  |  |  |
|  |  | Added February 2006 | 100 |  |  |  |  |  |  |
| 37 |  | Hook Groyne and Main Stopbank |  |  | 46450 |  |  |  |  |
|  |  | Point G-H 1030 lineal metres |  |  |  |  |  |  |  |
|  |  | of stopbank - average height 4 metres |  |  |  |  |  |  |  |
|  |  | topwidth 4 metres 2:1 batters |  |  |  |  |  |  |  |
|  |  | Stronghead and part of tail washed out. |  |  |  |  |  |  |  |
|  |  | 3000 cubic metres lost. |  |  |  |  |  |  |  |
|  |  | Stopbank width extend for rock stockpile |  |  | 1000 |  |  |  |  |
| 38 |  | Rock Stockpiles |  | 300 |  |  |  |  |  |
|  |  | Deducted January 2004 |  | -100 |  |  |  |  |  |
|  |  | Deducted January 2004 |  | -60 |  |  |  |  |  |
|  |  | Deducted February 2004 to #27 |  | -40 |  |  |  |  |  |
|  |  | Deducted February 2004 to #33 |  | -100 |  |  |  |  |  |
|  |  | Added April 2006 |  | 300 |  |  |  |  |  |
|  |  | Deducted December 2006 (To #41) |  | -80 |  |  |  |  |  |
| 39 |  | Rock rip rap - 250 lineal metres | 7000 |  |  |  |  |  |  |
|  |  | added 1998/1999 | 50 |  |  |  |  |  |  |
|  |  | Added December 2013 | 108 |  |  |  |  |  |  |
| 39 | a | Rock stockpile |  | 100 |  |  |  |  |  |
|  |  | taken 1998/1999 |  | -50 |  |  |  |  |  |
|  |  | Added April 2006 |  | 300 |  |  |  |  |  |
|  |  | Deducted September 2006 |  | -340 |  |  |  |  |  |
|  |  | Added May 2007 |  | 300 |  |  |  |  |  |
| 40 |  | Rock Stronghead (washed out Jan 1994) |  |  |  |  |  |  |  |
|  |  | Added October 2002 | 80 |  |  |  |  |  |  |
|  |  | Added January 2004 ex S/P #38 | 60 |  |  |  |  |  |  |
|  |  | Added April 2006 | 40 |  |  |  |  |  |  |
|  |  | Added November 2006 (Ex #13a) | 60 |  |  |  |  |  |  |
| 41 |  | Rock rip rap on inside of hook | 200 |  |  |  |  |  |  |
|  |  | groyne - 25 lineal metres |  |  |  |  |  |  |  |
|  |  | Rip rap extended upstream 100 metres | 2100 |  |  |  |  |  |  |
|  |  | Added December 2006 (Ex #13a) | 200 |  |  |  |  |  |  |
|  |  | Added December 2006 (Ex #55) | 360 |  |  |  |  |  |  |
|  |  | Added December 2006 (Ex #38) | 80 |  |  |  |  |  |  |
|  |  | Added December 2006 (Ex #55) | 552 |  |  |  |  |  |  |
|  |  | Added May 2007 | 400 |  |  |  |  |  |  |
|  |  | Added Sept 2009 Contract R 2009/12 - MBD | 600 |  |  |  |  |  |  |
| 42 |  | 6 rock spur groynes spaced |  |  |  |  |  |  |  |
|  |  | 20 metres apart with rip rap |  |  |  |  |  |  |  |
|  |  | between each groyne | 4150 |  |  |  |  |  |  |
|  |  | Added 31 October 2007 | 96 |  |  |  |  |  |  |
| 43 |  | Rock stockpile |  | 35 |  |  |  |  |  |
| 44 |  | Rock rip rap - 30 lineal metres | 200 |  |  |  |  |  |  |
|  |  | Added October 2002 | 740 |  |  |  |  |  |  |
| 45 |  | Rock protected spur stopbank |  |  | 750 |  |  |  |  |
|  |  | 15 Lineal metres | 1700 |  |  |  |  |  |  |
|  |  | Added April 2006 | 100 |  |  |  |  |  |  |
|  |  | Added May 2007 | 100 |  |  |  |  |  |  |
| 45 | a | Rock rip rap - 40 lineal metres added | 500 |  |  |  |  |  |  |
|  |  | Added September 2006 | 340 |  |  |  |  |  |  |
| 46 |  | Rock rip rap - 30 lineal metres | 300 |  |  |  |  |  |  |
|  |  | Added February 2006 | 300 |  |  |  |  |  |  |
| 46 | a | 4 Spur Groynes | 3000 |  |  |  |  |  |  |
|  |  | Added October 2002 | 60 |  |  |  |  |  |  |
|  |  | Added December 2004 ex S/P #55 | 120 |  |  |  |  |  |  |
|  |  | Added January 2005 ex S/P #55 | 550 |  |  |  |  |  |  |
| 46 | b | Deflector Groyne |  |  | 200 |  |  |  |  |
|  |  | Rock rip rap | 150 |  |  |  |  |  |  |
|  |  | added 1997/98 | 96 |  |  |  |  |  |  |
|  |  | Added October 2002 | 40 |  |  |  |  |  |  |
|  |  | Added January 2010 ex S/P # 55 - Arnold | 125 |  |  |  |  |  |  |
| 47 |  | Rock Protected Deflector Stopbank |  |  |  |  |  |  |  |
|  |  | 50 lineal metres, 4 metre topwidth |  |  |  |  |  |  |  |
|  |  | 1.5:1 batters, average height 3m |  |  | 1275 |  |  |  |  |
| 48 |  | Rock Stronghead | 2100 |  |  |  |  |  |  |
|  |  | Added November 2008 - Ex Stockpile #49a (Arnold) | 60 |  |  |  |  |  |  |
|  |  | Added May 2009 - Ex Wanganui Stockpile | 10 |  |  |  |  |  |  |
|  |  | Added February 2014 | 144 |  |  |  |  |  |  |
| 49 |  | Rock rip rap - 50 lineal metres | 1200 |  |  |  |  |  |  |
|  |  | Added 31 October 2007 | 50 |  |  |  |  |  |  |
|  |  | Added February 2008 ex stockpile 49a | 250 |  |  |  |  |  |  |
|  |  | Added February 2008 ex # 55 | 20 |  |  |  |  |  |  |
|  |  | Added November 2008 Contract R 2008 / 11 | 300 |  |  |  |  |  |  |
|  |  | Added August 2009 ex # 55 - Arnold Contracting | 300 |  |  |  |  |  |  |
|  |  | Added Sept 2009 Contract R 2009/12 - MBD | 18 |  |  |  |  |  |  |
|  |  | Added over 60m Jan 2010- Arnold R 2010.3 | 924 |  |  |  |  |  |  |
|  |  | Added December 2013 | 540 |  |  |  |  |  |  |
| 49 | a | New Stockpile Added May 2007 |  | 100 |  |  |  |  |  |
|  |  | Added 31 October 2007 |  | 150 |  |  |  |  |  |
|  |  | Deducted February 2008 - Contract R 2008/1 |  | -250 |  |  |  |  |  |
|  |  | Added July 2008 - Contract R 2008 / 4 |  | 250 |  |  |  |  |  |
|  |  | Deducted November 2008 to #48 Emergency (Arnold) |  | -60 |  |  |  |  |  |
|  |  | New Stockpile Added January 2010 - Arnold R 2010.3 |  | 100 |  |  |  |  |  |
| 49 | b | New spur added 31 October 2007 | 280 |  |  |  |  |  |  |
| 49 | c | New Rip rap added November 2008 Contract R2008/11 | 970 |  |  |  |  |  |  |
|  |  | Added January 2014 | 288 |  |  |  |  |  |  |
|  |  | Added May 2014 - Topup over 40m 2014/14 | 648 |  |  |  |  |  |  |
| 50 |  | Rock Protected Deflector Stopbank |  |  |  |  |  |  |  |
|  |  | 50 lineal metres, 4 metre topwidth |  |  |  |  |  |  |  |
|  |  | 1.5:1 batters, average height 3.5m |  |  | 1650 |  |  |  |  |
| 51 |  | Rock Stronghead | 3000 |  |  |  |  |  |  |
|  |  | Added July 2003 | 100 |  |  |  |  |  |  |
| 52 |  | Rock rip rap - 150 lineal metres |  |  |  |  |  |  |  |
|  |  | 20 tonne/metre | 3000 |  |  |  |  |  |  |
|  |  | Added February 2014 | 360 |  |  |  |  |  |  |
|  |  | Added November 2008 Contract R 2008 / 11 | 80 |  |  |  |  |  |  |
| 53 |  | Rock Spur Groyne | 200 |  |  |  |  |  |  |
| 54 |  | Rock Protected Spur Bank |  |  |  |  |  |  |  |
|  |  | 15 Lineal metres, 4 metres topwidth |  |  |  |  |  |  |  |
|  |  | 1.5:1 batters. Average height 4m |  |  |  |  |  |  |  |
|  |  | Plus rock protection along bank, |  |  |  |  |  |  |  |
|  |  | 70 lineal metres | 3400 |  | 600 |  |  |  |  |
|  |  | added 1997/98 | 150 |  |  |  |  |  |  |
|  |  | Added April 2006 | 150 |  |  |  |  |  |  |
| 55 |  | Rock stockpiles |  | 700 |  |  |  |  |  |
|  |  | taken 1997/98 |  | -186 |  |  |  |  |  |
|  |  | added 1999/2000 |  | 200 |  |  |  |  |  |
|  |  | Deducted December 2004 to #46a |  | -120 |  |  |  |  |  |
|  |  | Deducted January 2005 to #46a |  | -550 |  |  |  |  |  |
|  |  | Added April 2006 |  | 500 |  |  |  |  |  |
|  |  | Deducted December 2006 (To #41) |  | -360 |  |  |  |  |  |
|  |  | Added December 2006 |  | 552 |  |  |  |  |  |
|  |  | Deducted December 2006 (To #41) |  | -552 |  |  |  |  |  |
|  |  | Added May 2007 |  | 500 |  |  |  |  |  |
|  |  | Deducted February 2008 to #49 |  | -20 |  |  |  |  |  |
|  |  | Deducted February 2008 to #51 |  | -200 |  |  |  |  |  |
|  |  | Added July 2008 - Contract R 2008 / 4 |  | 220 |  |  |  |  |  |
|  |  | Added July 2008 - Contract R 2008 / 4 |  | 1,000 |  |  |  |  |  |
|  |  | Deducted August 2009 to # 49 - Arnold Contracting |  | -300 |  |  |  |  |  |
|  |  | Added Sept 2009 Contract R 2009/12 - MBD |  | 300 |  |  |  |  |  |
|  |  | Deducted December 2009 - to # 21 - Henry Adams |  | -54 |  |  |  |  |  |
|  |  | Deducted January 2010 - to # 46b - Arnold |  | -125 |  |  |  |  |  |
|  |  | Added Sept '10 - Arnold R 2010.16 |  | 400 |  |  |  |  |  |
|  |  | Added December 2013 |  | 414 |  |  |  |  |  |
| 56 |  | Rock Stronghead (Washed out Jan.1994) |  |  |  |  |  |  |  |
|  |  | Stronghead reconstructed at end of new |  |  |  |  |  |  |  |
|  |  | bank | 500 |  |  |  |  |  |  |
|  |  | added 1998/1999 | 100 |  |  |  |  |  |  |
| 56 | a | Riprap added Sept 2010 - 120m Stewarts - Arnold | 550 |  |  |  |  |  |  |
|  |  | Added October 2013 | 286 |  |  |  |  |  |  |
| 57 |  | Rock Protection Deflector |  |  | 1800 |  |  |  |  |
|  |  | Stopbank - 40 lineal metres | 2450 |  |  |  |  |  |  |
|  |  | 4 metres topwidth, 1.5:1 batters |  |  |  |  |  |  |  |
|  |  | height 3.0 metres average. |  |  |  |  |  |  |  |
|  |  | Stopbank washed out over 50 metres |  |  |  |  |  |  |  |
|  |  | Jan 1994. Replaced over 30 metres. |  |  |  |  |  |  |  |
|  |  | Rock added from stockpile (15) | 674 |  |  |  |  |  |  |
|  |  | added 1999/2000 | 20 |  |  |  |  |  |  |
| 57 | a | New Riprap over 300 lineal metres added May 2009 |  |  |  |  |  |  |  |
|  |  | Ex Wanganui Stockpile - Contract R 2009 / 6 | 3184 |  |  |  |  |  |  |
|  |  | Ex Wanganui Quarry - Contract R 2009 / 6 | 270 |  |  |  |  |  |  |
|  |  | Ex Wanganui Stockpile - Contract R 2009 / 6 |  |  |  |  | 50 |  |  |
|  |  | AddedSept '10 - R 2010.16 - Arnold | 60 |  |  |  |  |  |  |
|  |  | Extended November 2012 over 100m - MBD | 2000 |  |  |  |  |  |  |
| 58 |  | Main stopbank - Point H-I |  |  |  |  |  |  |  |
|  |  | 1200 lineal metres, 4 metre topwidth |  |  |  |  |  |  |  |
|  |  | 2:1 batters, height 3.5 metres average |  |  | 46000 |  |  |  |  |
|  |  | 230 metres destroyed may 2009 |  |  | -10000 |  |  |  |  |
|  |  | Repaired Contract R 2009/6 Henry Adams - May 2009 |  |  | 10000 |  |  |  |  |
| 59 |  | Rock Protected Deflector Groyne |  |  |  |  |  |  |  |
|  |  | 40 lineal metres |  |  |  |  |  |  |  |
|  |  | 4 metre topwidth, 1.5:1 batters |  |  |  |  |  |  |  |
|  |  | height 4 metres average. | 2000 |  | 1600 |  |  |  |  |
|  |  | added 1999/2000 | 50 |  |  |  |  |  |  |
|  |  | AddedSept '10 - R 2010.16 - Arnold | 100 |  |  |  |  |  |  |
|  |  | Added December 2013 | 1728 |  |  |  |  |  |  |
|  |  | Topup March 2015 | 100 |  |  |  |  |  |  |
| 59 | a | Rock Spur Groyne | 250 |  |  |  |  |  |  |
|  |  | added 1999/2000 | 50 |  |  |  |  |  |  |
| 59 | b | Rock rip rap | 500 |  |  |  |  |  |  |
|  |  | added 1997/98 | 70 |  |  |  |  |  |  |
|  |  | added 1999/2000 | 50 |  |  |  |  |  |  |
| 60 |  | Rock Protected Deflector Bank |  |  |  |  |  |  |  |
|  |  | 80 lineal metres |  |  |  |  |  |  |  |
|  |  | 4 metre topwidth, 1.5:1 batters |  |  |  |  |  |  |  |
|  |  | height 3 metres, 40 lineal metres |  |  |  |  |  |  |  |
|  |  | rip rap | 600 |  | 2050 |  |  |  |  |
|  |  | Added December 2010 - Arnold (Ex Sullivan's) | 438 |  |  |  |  |  |  |
| 61 |  | Crate Groyne Stronghead with rock |  |  |  |  |  |  |  |
|  |  | protection | 2500 |  |  |  |  |  |  |
|  |  | Added April-May 2011 R 2011.2 - Westland | 414 |  |  |  |  |  |  |
|  |  | Topup over 20m March 2015 | 264 |  |  |  |  |  |  |
|  |  | RIGHT BANK |  |  |  |  |  |  |  |
| 62 |  | Rock retard - right bank |  |  |  |  |  |  |  |
|  |  | 80 lineal metres | 1500 |  |  |  |  |  |  |
| 63 |  | Rock retard - right bank | 1200 |  |  |  |  |  |  |
|  |  | 60 lineal metres |  |  |  |  |  |  |  |
|  |  | Rock added to retard | 200 |  |  |  |  |  |  |
|  |  | Added July 2003 | 200 |  |  |  |  |  |  |
|  |  | Added September 2011 - Arnold (Ex McGrath's) | 58 |  |  |  |  |  |  |
| 64 |  | Post and rail retard |  |  |  |  |  |  |  |
|  |  | 350 lineal metres (Valuation June 1993 - |  |  |  |  |  |  |  |
|  |  | $5,000.00) |  |  |  | 10,000.00 |  |  |  |
|  |  | Added September 2011 - Arnold (ex McGrath's) | 50 |  |  |  |  |  |  |
| 65 |  | Old rock retard - 150 lineal metres | 1600 |  |  |  |  |  |  |
|  |  | added 1998/1999 | 312 |  |  |  |  |  |  |
|  |  | Added October 2004 | 200 |  |  |  |  |  |  |
|  |  | AddedSept '10 - R 2010.16 - Arnold | 250 |  |  |  |  |  |  |
|  |  | Added September 2011 - Arnold (ex McGrath's) | 100 |  |  |  |  |  |  |
|  |  | Added January 2012 - Westland Con (Ex Ianthe) | 1260 |  |  |  |  |  |  |
|  |  | Added January 2012 - Westland Con (Ex Whataroa) | 1290 |  |  |  |  |  |  |
|  |  | Added December 2013 | 216 |  |  |  |  |  |  |
| 66 |  | Stopbank - Point J-K |  |  |  |  |  |  |  |
|  |  | 850 lineal metres 4 metres |  |  |  |  |  |  |  |
|  |  | topwidth 2:1 batters |  |  |  |  |  |  |  |
|  |  | height 4.5 metres average |  |  | 50000 |  |  |  |  |
| 67 |  | Rock rip rap on Stopbank |  |  |  |  |  |  |  |
|  |  | 850 lineal metres | 12072 |  |  |  |  |  |  |
|  |  | added 1997/98 | 200 |  |  |  |  |  |  |
|  |  | Added October 2002 | 700 |  |  |  |  |  |  |
|  |  | Added October 2004 | 200 |  |  |  |  |  |  |
|  |  | Added November 2012-WCL (Ex Ianthe) | 130 |  |  |  |  |  |  |
| 67 | a | Add New Stockpile - November 2012- WCL (Ex Ianthe) |  | 100 |  |  |  |  |  |
| 68 |  | Rock Protected Stronghead | 4000 |  |  |  |  |  |  |
|  |  | added 1999/2000 | 200 |  |  |  |  |  |  |
| 69 |  | 2/100 tonne spur groynes | 200 |  |  |  |  |  |  |
| 70 |  | Rock Protected Stronghead | 3500 |  |  |  |  |  |  |
| 70 | a | New Stockpile Added May 2007 |  | 200 |  |  |  |  |  |
| 71 |  | Hook Groynes and Stopbanking |  |  |  |  |  |  |  |
|  |  | Point K-L 500 lineal metres |  |  |  |  |  |  |  |
|  |  | height 4.5 metres average |  |  |  |  |  |  |  |
|  |  | 4 metre topwidth, 2:1 batters |  |  | 29500 |  |  |  |  |
| 72 |  | Spur Groyne | 100 |  |  |  |  |  |  |
|  |  | Added July 2003 | 140 |  |  |  |  |  |  |
|  |  | Added September 2005 | 60 |  |  |  |  |  |  |
| 72 | b | Added 31 October 2007 | 388 |  |  |  |  |  |  |
| 72 | c | Added 31 October 2007 | 392 |  |  |  |  |  |  |
| 73 |  | Rock Retard | 1412 |  |  |  |  |  |  |
|  |  | Added September 2005 | 250 |  |  |  |  |  |  |
|  |  | Added December 2005 | 1050 |  |  |  |  |  |  |
|  |  | Added April 2006 | 300 |  |  |  |  |  |  |
|  |  | Added May 2007 | 300 |  |  |  |  |  |  |
| 73 | a | Spur Groyne added | 60 |  |  |  |  |  |  |
| 73 | b | Rip rap added September 2005 | 96 |  |  |  |  |  |  |
| 73 | c | Rock Spur added December 2005 | 180 |  |  |  |  |  |  |
| 73 | d | Rock Spur added December 2005 | 180 |  |  |  |  |  |  |
|  |  | EVANS CREEK |  |  |  |  |  |  |  |
| 74 |  | Rock Stockpile |  | 380 |  |  |  |  |  |
|  |  | taken 1997/1998 |  | -120 |  |  |  |  |  |
| 75 |  | 8/60 tonne rock spur groynes | 600 |  |  |  |  |  |  |
|  |  | added 1997/98 | 120 |  |  |  |  |  |  |
| 76 |  | 8/60 tonne rock spur groynes | 480 |  |  |  |  |  |  |
|  |  | LEFT BANK |  |  |  |  |  |  |  |
| 77 |  | Rock Spur Groyne | 250 |  |  |  |  |  |  |
| 78 |  | Rock Deflector Groyne | 500 |  |  |  |  |  |  |
| 79 |  | Rock Deflector Groyne | 1000 |  |  |  |  |  |  |
| 80 |  | Rock Retard | 500 |  |  |  |  |  |  |
| 81 |  | Rock rip rap - 100 lineal metres | 1000 |  |  |  |  |  |  |
| 82 |  | Rock Spur Groyne | 300 |  |  |  |  |  |  |
| 83 |  | Rock rip rap - 180 lineal metres | 1200 |  |  |  |  |  |  |
| 84 |  | Main stopbank - Point I-M |  |  |  |  |  |  |  |
|  |  | 2500 lineal metres |  |  |  |  |  |  |  |
|  |  | 4 metre topwidth, 2:1 batters |  |  |  |  |  |  |  |
|  |  | height 3 metres |  |  | 75000 |  |  |  |  |
| 85 |  | Rock rip rap - 10 lineal metres | 100 |  |  |  |  |  |  |
| 86 |  | Rock Spur Groyne | 100 |  |  |  |  |  |  |
| 87 |  | Rock rip rap - 90 lineal metres | 1350 |  |  |  |  |  |  |
| 88 |  | Rock reatard - 250 lineal metres | 5000 |  |  |  |  |  |  |
| 89 |  | Rock rip rap along tail of hook groyne |  |  |  |  |  |  |  |
|  |  | 300 lineal metres | 6000 |  |  |  |  |  |  |
| 90 |  | Stronghead of hook groyne | 4000 |  |  |  |  |  |  |
| 91 |  | Stopbank Point M-N |  |  |  |  |  |  |  |
|  |  | Hook Groyne and Training wall |  |  |  |  |  |  |  |
|  |  | 4 metre topwidth |  |  |  |  |  |  |  |
|  |  | 2:1 batters, height 4 metres |  |  |  |  |  |  |  |
|  |  | average, 720 lineal metres |  |  | 34600 |  |  |  |  |
| 92 |  | Rock rip rap - 500 lineal metres | 3500 |  |  |  |  |  |  |
| 93 |  | Old rock retard - 10 lineal metres | 50 |  |  |  |  |  |  |
| 94 |  | Rock rip rap - 750 lineal metres | 7500 |  |  |  |  |  |  |
| 95 |  | Main stopbank - Point M-O. Average |  |  |  |  |  |  |  |
|  |  | height 2 metres, 4 metres topwidth |  |  |  |  |  |  |  |
|  |  | 2:1 batters, 2600 lineal metres |  |  | 41600 |  |  |  |  |
| 96 |  | Rock Retard - 135 lineal metres | 5180 |  |  |  |  |  |  |
|  |  | Added November 2012 - WCL (Ex Ianthe) | 400 |  |  |  |  |  |  |
| 97 |  | Rock Spur Groyne | 550 |  |  |  |  |  |  |
| 98 |  | Rock Spur Groyne | 750 |  |  |  |  |  |  |
|  |  | added 1998/1999 | 150 |  |  |  |  |  |  |
| 99 |  | Rock Spur Groyne | 650 |  |  |  |  |  |  |
|  |  | added 1998/1999 | 150 |  |  |  |  |  |  |
| 100 |  | Rock Spur Groyne | 600 |  |  |  |  |  |  |
| 101 |  | Rock Spur Groyne and 15 lineal metres |  |  |  |  |  |  |  |
|  |  | rock rip rap | 650 |  |  |  |  |  |  |
| 102 |  | Rock Spur Groyne | 1000 |  |  |  |  |  |  |
|  |  | added 1998/1999 | 100 |  |  |  |  |  |  |
| 103 |  | Rock rip rap - 50 lineal metres | 500 |  |  |  |  |  |  |
|  |  | added 1998/1999 | 100 |  |  |  |  |  |  |
| 104 |  | Rock Spur Groyne | 750 |  |  |  |  |  |  |
| 105 |  | Rock Spur Groyne | 1150 |  |  |  |  |  |  |
|  |  | added 1998/1999 | 60 |  |  |  |  |  |  |
| 106 |  | Wire Crates facing stopbank over |  |  |  |  |  |  |  |
|  |  | 120 lineal metres | 300 |  |  |  |  |  |  |
| 107 |  | Main stopbank - Point P-Q |  |  |  |  |  |  |  |
|  |  | Bottom of stopbank faced with wire |  |  |  |  |  |  |  |
|  |  | crates. Top 2 metres faced with rock |  |  |  |  |  |  |  |
|  |  | rubble. 4 metre topwidth 2:1 batters, |  |  |  |  |  |  |  |
|  |  | height 2 metres, 200 lineal metres |  |  | 3200 |  | 400 |  |  |
|  |  | RIGHT BANK |  |  |  |  |  |  |  |
| 108 |  | Stopbank - Right Bank Point R-S |  |  |  |  |  |  |  |
|  |  | 350 lineal metres, height 4.5 metres |  |  |  |  |  |  |  |
|  |  | 4 metres topwidth 2:1 batters |  |  | 20500 |  |  |  |  |
| 109 |  | Rock rip rap on edge of Stopbank | 6950 |  |  |  |  |  |  |
|  |  | 350 lineal metres |  |  |  |  |  |  |  |
|  |  | Rock added to rip rap | 300 |  |  |  |  |  |  |
| 110 |  | Rock stronghead - Point S | 2000 |  |  |  |  |  |  |
| 111 |  | Stopbank and Hook Groyne |  |  |  |  |  |  |  |
|  |  | Point S-T - 150 lineal metres |  |  |  |  |  |  |  |
|  |  | Average Height 4.5 metres |  |  |  |  |  |  |  |
|  |  | 4 metres topwidth 2:1 batters |  |  | 9000 |  |  |  |  |
| 112 |  | Rock rip rap - 400 lineal metres | 6050 |  |  |  |  |  |  |
| 113 |  | Rock rip rap and willows |  |  |  |  |  |  |  |
|  |  | 200 lineal metres | 3000 |  |  |  |  |  |  |
| 114 |  | Rock Spur Groyne | 2000 |  |  |  |  |  |  |
| 115 |  | Rock rip rap - 5 lineal metres | 800 |  |  |  |  |  |  |
|  |  | Added October 2002 | 120 |  |  |  |  |  |  |
| 116 |  | Rock retard - 70 lineal metres | 700 |  |  |  |  |  |  |
| 117 |  | Stopbank - Right Bank |  |  | 9500 |  |  |  |  |
|  |  | height 4.5 metres, topwidth |  |  |  |  |  |  |  |
|  |  | 4 metres, 2:1 batters |  |  |  |  |  |  |  |
|  |  | 250 lineal metres |  |  |  |  | 750 |  |  |
| 118 |  | Rock rip rap - 265 lineal metres | 9600 |  |  |  |  |  |  |
|  |  | added 1997/98 | 200 |  |  |  |  |  |  |
|  |  | added 1998/1999 | 270 |  |  |  |  |  |  |
|  |  | Added September 2001 | 150 |  |  |  |  |  |  |
|  |  | Added July 2003 | 232 |  |  |  |  |  |  |
|  |  | Added November 2012 - WCL | 80 |  |  |  |  |  |  |
| 119 |  | Rock Spur Groyne | 1500 |  |  |  |  |  |  |
| 120 |  | 2/300 tonne Rock Spur Groynes | 600 |  |  |  |  |  |  |
| 121 |  | Rock Spur Groyne | 300 |  |  |  |  |  |  |
| 121 | a | Rock Spur Groyne | 300 |  |  |  |  |  |  |
| 122 |  | Rock Spur Groyne | 200 |  |  |  |  |  |  |
| 123 |  | Rock Spur Groyne | 250 |  |  |  |  |  |  |
| 124 |  | Rock Spur Groyne | 260 |  |  |  |  |  |  |
| 125 |  | Rock Spur Groyne | 300 |  |  |  |  |  |  |
| 126 |  | 2/300 tonne Rock Spur Groynes | 600 |  |  |  |  |  |  |
|  |  | added 1997/98 | 100 |  |  |  |  |  |  |
| 127 |  | Rock Rip rap - 25 lineal metres | 150 |  |  |  |  |  |  |
|  |  | added 1997/98 | 100 |  |  |  |  |  |  |
| 128 |  | Rock Spur Groyne | 100 |  |  |  |  |  |  |
| 128 | a | Stockpile |  | 1000 |  |  |  |  |  |
|  |  | taken 1997/98 |  | -200 |  |  |  |  |  |
|  |  | taken 1997/98 |  | -186 |  |  |  |  |  |
|  |  | DRAINAGE |  |  |  |  |  |  |  |
| 129 |  | Drain L5 - Start to Junction with L7 |  |  |  |  |  |  |  |
|  |  | 1000 lineal metres |  |  |  |  |  |  |  |
|  |  | 2 metre bedwidth 2:1 batter 1 m deep |  |  |  |  |  | 4000 |  |
| 130 |  | Drain L9 - 160 lineal metres |  |  |  |  |  |  |  |
|  |  | 1 metre bedwidth, 0.75 metres deep |  |  |  |  |  |  |  |
|  |  | 2:1batters |  |  |  |  |  | 270 |  |
| 131 |  | Drain L8 - 16 lineal metres |  |  |  |  |  |  |  |
|  |  | 1 metre bedwidth, 0.75 metres deep |  |  |  |  |  |  |  |
|  |  | 2:1batters |  |  |  |  |  | 300 |  |
| 132 |  | Drain L7 - 300 lineal metres |  |  |  |  |  |  |  |
|  |  | 1 metre bedwidth, 1 metre deep |  |  |  |  |  |  |  |
|  |  | 2:1batters |  |  |  |  |  | 900 |  |
| 133 |  | Drain L5 - From Junction with L5 to L6 |  |  |  |  |  |  |  |
|  |  | 500 lineal metres, 3 metres bedwdth, |  |  |  |  |  |  |  |
|  |  | 1metre deep, 2:1 batters |  |  |  |  |  | 2500 |  |
| 134 |  | Drain L6 - 900 lineal metes, 1 metre |  |  |  |  |  |  |  |
|  |  | bedwidth, 1 metre deep, 2:1 batters |  |  |  |  |  | 2700 |  |
| 135 |  | Drain L5 from L6-L2, 1300 lineal metres |  |  |  |  |  |  |  |
|  |  | 4 metre bedwidth, 1 metre deep, |  |  |  |  |  |  |  |
|  |  | 2:1 batters |  |  |  |  |  | 7800 |  |
| 136 |  | Drain L4 along toe of hill, 1800 lineal |  |  |  |  |  |  |  |
|  |  | metrs, 1 metre bedwidth, 1.5 metres deep, |  |  |  |  |  |  |  |
|  |  | 1.5:1 batters |  |  |  |  |  | 8800 |  |
| 137 |  | Drain L2, 1000 lineal metres, 3 metres |  |  |  |  |  |  |  |
|  |  | bedwidth, 1.5 metres deep, 1.5:1batters |  |  |  |  |  | 7900 |  |
| 138 |  | Graham's Creek - 1400 lineal metres, |  |  |  |  |  |  |  |
|  |  | 1.5 metres bedwidth, 1.5 metres deep |  |  |  |  |  |  |  |
|  |  | 1.5:1 batters |  |  |  |  |  |  | 1400.00 |
| 139 |  | Side drain to Grahams Creek |  |  |  |  |  |  |  |
|  |  | 400 lineal metres, 1 metre bedwidth |  |  |  |  |  |  |  |
|  |  | 1.5 metres deep, 1.5:1 batters |  |  |  |  |  | 2000 |  |
| 140 |  | Side drain to Grahams Creek |  |  |  |  |  |  |  |
|  |  | 440 lineal metres, 1 metre bedwidth |  |  |  |  |  |  |  |
|  |  | 1.5 metres deep, 1.5:1 batters |  |  |  |  |  | 2150 |  |
| 141 |  | Side drain to Grahams Creek |  |  |  |  |  |  |  |
|  |  | 850 lineal metres, 1 metre bedwidth |  |  |  |  |  |  |  |
|  |  | 1.5 metres deep, 1.5:1 batters |  |  |  |  |  | 4150 |  |
| 142 |  | Drain GR1 Grahams Creek |  |  |  |  |  |  |  |
|  |  | 660 lineal metres, 1 metre bedwidth |  |  |  |  |  |  |  |
|  |  | 1.5 metres deep, 1.5:1 batters |  |  |  |  |  | 3200 |  |
| 143 |  | Ash Creek - 400 lineal metres to rating |  |  |  |  |  |  |  |
|  |  | boundary, 1.5 metre bedwidth 2 metres deep |  |  |  |  |  |  |  |
|  |  | 1.5:1 batters |  |  |  |  |  |  | 400.00 |
| 144 |  | Gee Creek - 1100 lineal metres, 1.5 metres |  |  |  |  |  |  |  |
|  |  | bedwidth, 2.5 metres deep |  |  |  |  |  |  |  |
|  |  | 1.5:1 batters |  |  |  |  |  |  | 1100.00 |
| 145 |  | Drain G1 to Gee Creek - 450 lineal metres - |  |  |  |  |  |  |  |
|  |  | 1 metre bedwidth, 1.5 deep |  |  |  |  |  |  |  |
|  |  | 1.5:1 batters |  |  |  |  |  | 2200 |  |
| 146 |  | Side drain to Gee Creek, 150 lineal metres, |  |  |  |  |  |  |  |
|  |  | 1 metre bedwidth, 1.5 deep |  |  |  |  |  |  |  |
|  |  | 1.5:1 batters |  |  |  |  |  | 750 |  |
| 147 |  | Side drain to Gee Creek, 450 lineal metres |  |  |  |  |  |  |  |
|  |  | 1.5 metres deep, 1 metre bedwidth |  |  |  |  |  |  |  |
|  |  | 1.5:1 batters |  |  |  |  |  | 2200 |  |
| 148 |  | Drain G4 to Gee Creek, 640 lineal metres, |  |  |  |  |  |  |  |
|  |  | 1.5 deep, 1 metre bedwidth, |  |  |  |  |  |  |  |
|  |  | 1.5:1 batters |  |  |  |  |  | 3100 |  |
| 149 |  | Drain G3 to Gee Creek, 560 lineal metres, |  |  |  |  |  |  |  |
|  |  | 1 metre bedwidth, 1.5 metres deep, |  |  |  |  |  |  |  |
|  |  | 1.5:1 batters |  |  |  |  |  | 2700 |  |
| 150 |  | St George Creek, from junction with |  |  |  |  |  |  |  |
|  |  | La Fontaine Creek to Wanganui Flat Road |  |  |  |  |  |  |  |
|  |  | 4 metres bedwidth, 1.5 metres deep, |  |  |  |  |  |  |  |
|  |  | 1.5:1 batters, 1700 lineal metres |  |  |  |  |  |  | 1700.00 |
| 151 |  | St George Creek, Wanganui Flat road up to |  |  |  |  |  |  |  |
|  |  | Junction with Harold Creek 1400 lineal |  |  |  |  |  |  |  |
|  |  | metres, 3 metres bedwidth, 1.5 metres deep |  |  |  |  |  |  |  |
|  |  | 1.5:1 batters |  |  |  |  |  |  | 1400.00 |
| 152 |  | St George Creek from Harold Creek to State |  |  |  |  |  |  |  |
|  |  | Highway, 2100 lineal metres, 1 metre |  |  |  |  |  |  |  |
|  |  | bedwidth, 1 metre deep, 1.5:1 batters |  |  |  |  |  |  | 2100.00 |
| 153 |  | Factory Creek, 800 lineal metres, 3 metres |  |  |  |  |  |  |  |
|  |  | bedwidth, 1.5 metres deep, 1.5:1batters |  |  |  |  |  |  | 800.00 |
| 154 |  | Side drain to La Fontaine St., 200 lineal |  |  |  |  |  |  |  |
|  |  | metres, 1 metre bedwidth, 1 metre deep, |  |  |  |  |  |  |  |
|  |  | 1.5:1 batters |  |  |  |  |  | 500 |  |
| 155 |  | Side drain to La Fontaine St. (Levetts |  |  |  |  |  |  |  |
|  |  | Drainage), 1900 lineal metres, 1 metre |  |  |  |  |  |  |  |
|  |  | bedwidth, 1.5 deep, 1.5:1 batters |  |  |  |  |  | 9250 |  |
| 156 |  | Thorpes Creek, 2660 lineal metres, 2 metre |  |  |  |  |  |  |  |
|  |  | bedwidth, 2 metres deep, 0.5:1 batters |  |  |  |  |  |  | 2660.00 |
| 157 |  | Side drain to Thorpes Creek, 900 lineal |  |  |  |  |  |  |  |
|  |  | metres, 1 metre bedwidth, 1.5 deep |  |  |  |  |  |  |  |
|  |  | 1.5:1 batters |  |  |  |  |  | 4400 |  |
| 158 |  | Drain B1, 800 lineal metres, 1 metre |  |  |  |  |  |  |  |
|  |  | bedwidth, 1.5 metres deep, 1.5:1batters |  |  |  |  |  | 3900 |  |
| 159 |  | Drain T2 - 300 lineal metres 1 metre |  |  |  |  |  |  |  |
|  |  | bedwidth, 1.5 deep, 1.5:1 batters |  |  |  |  |  | 1450 |  |
| 160 |  | La Fontaine St, 5360 lineal metres, 10 |  |  |  |  |  |  |  |
|  |  | metres bedwidth, 2.5 metres deep |  |  |  |  |  |  |  |
|  |  | 1.5:1 batters |  |  |  |  |  |  | 5360.00 |
| 161 |  | Side drain to La Fontaine St, 1100 lineal |  |  |  |  |  |  |  |
|  |  | metres, 1 metre bedwidth, 1.5 metres deep |  |  |  |  |  |  |  |
|  |  | 1.5:1 batters |  |  |  |  |  | 5350 |  |
| 162 |  | Drain 1 300 lineal metres, 1 metre bedwidth |  |  |  |  |  |  |  |
|  |  | 1.5 deep, 1.5:1 batters |  |  |  |  |  | 1460 |  |
| 163 |  | Drain A. 240 lineal metres, 1 metre bedwidth |  |  |  |  |  |  |  |
|  |  | 1.5 deep, 1.5:1 batters |  |  |  |  |  | 1170 |  |
| 164 |  | Drain 2, 450 lineal metres, 2 metre bedwidth |  |  |  |  |  |  |  |
|  |  | 2 metres deep, 1.5:1 batters |  |  |  |  |  | 4500 |  |
| 165 |  | Drain B./500 lineal metes, 1 metre bedwidth |  |  |  |  |  |  |  |
|  |  | 1.5 metres deep, 1.5:1 batters |  |  |  |  |  | 2440 |  |
| 166 |  | Drain 3, 600 lineal metres, 1 metre bedwidth, |  |  |  |  |  |  |  |
|  |  | 1.5 metres deep, 1.5:1 batters |  |  |  |  |  | 2920 |  |
| 167 |  | Drain C. 700 lineal metres, 1 metre deep, |  |  |  |  |  |  |  |
|  |  | 1 metre bedwidth, 1.5:1 batters |  |  |  |  |  | 1750 |  |
| 168 |  | Drain 4, 740 lineal metres, 1 metre deep, |  |  |  |  |  |  |  |
|  |  | 1 metre bedwidth, 1.5:1 batters |  |  |  |  |  | 3600 |  |
| 169 |  | Wingham Creek, 3200 lineal metres, |  |  |  |  |  |  |  |
|  |  | 2 metres bedwidth, 1.5 metres deep, |  |  |  |  |  |  |  |
|  |  | 1.5:1 batters |  |  |  |  |  |  | 3200.00 |
| 170 |  | Black Creek, 2900 lineal metres, 1 metres |  |  |  |  |  |  |  |
|  |  | bedwidth, 2 metres deep, 1.5:1 batters |  |  |  |  |  |  | 2900.00 |
| 171 |  | Main Road Drain, LHS, 2900 lineal metres, |  |  |  |  |  |  |  |
|  |  | 1 metre bedwidth, 2 metres deep, |  |  |  |  |  |  |  |
|  |  | 1.5:1 batters |  |  |  |  |  | 23200 |  |
| 172 |  | Side drain, 700 lineal metres 1 metre |  |  |  |  |  |  |  |
|  |  | bedwidth, 2 metres deep |  |  |  |  |  | 5600 |  |
| 173 |  | Side drain - 600 lineal metres, 1 metre |  |  |  |  |  |  |  |
|  |  | bedwidth, 2 metres deep, 1.5:1 batters |  |  |  |  |  | 4800 |  |
| 174 |  | Side drain, 500 lineal metres, 1 metre |  |  |  |  |  |  |  |
|  |  | bedwidth, 2 metres deep, 1.5:1 batters |  |  |  |  |  | 4000 |  |
| 175 |  | Side drain, 400 lineal metres 1 metre |  |  |  |  |  |  |  |
|  |  | bedwidth, 2 metres deep, 1.5:1 batters |  |  |  |  |  | 3200 |  |
| 176 |  | Main Road Drain, RHS, 3000 lineal metres, |  |  |  |  |  |  |  |
|  |  | 1 metre bedwidth, 2 metres deep, |  |  |  |  |  |  |  |
|  |  | 1.5:1 batters |  |  |  |  |  | 24000 |  |
| 177 |  | Side drain, 800 lineal metres, 1 metre |  |  |  |  |  |  |  |
|  |  | bedwidth, 2 metres deep, 1.5:1 batters |  |  |  |  |  | 6400 |  |
| 178 |  | Side drain, 460 lineal metres, 1 metre |  |  |  |  |  |  |  |
|  |  | bedwidth, 2 metres deep, 1.5:1 batters |  |  |  |  |  | 3680 |  |
| 179 |  | Cowhide Creek, below S/H, 700 lineal |  |  |  |  |  |  |  |
|  |  | metres, 2 metres below bedwidth, 1 metre |  |  |  |  |  |  |  |
|  |  | deep 1.5:1 batters |  |  |  |  |  | 2500 |  |
| 180 |  | Creek, 500 lineal metres, 2 metre bedwidth |  |  |  |  |  |  |  |
|  |  | 1 metre deep, 1.5:1 batters |  |  |  |  |  |  | 500.00 |
| 181 |  | Side drain, 900 lineal metres, 1 metre |  |  |  |  |  |  |  |
|  |  | bedwidth, 1 metre deep, 1.5:1 batters |  |  |  |  |  | 2250 |  |
| 182 |  | Side drain 1000 lineal metres 1 metres |  |  |  |  |  |  |  |
|  |  | bedwidth, 1 metre deep, 1.5:1 batters |  |  |  |  |  | 2500 |  |
| 183 |  | Side drain, 400 lineal metres |  |  |  |  |  |  |  |
|  |  | 1 metres bedwidth, 1 metre deep |  |  |  |  |  |  |  |
|  |  | 1.5:1 batters |  |  |  |  |  | 1000 |  |
|  |  | ADDITIONS: LA FONTAINE STREAM |  |  |  |  |  |  |  |
| 184 |  | 4 Rock spur groynes | 200 |  |  |  |  |  |  |
| 185 |  | Rip rap - 15 lineal metres | 100 |  |  |  |  |  |  |
| 186 |  | Rip rap - 30 lineal metres | 150 |  |  |  |  |  |  |
| 187 |  | 7 Rock spur groynes | 350 |  |  |  |  |  |  |
| 188 |  | 5 rock spur groynes | 250 |  |  |  |  |  |  |
|  |  | Added June 2009 - Arnold Contracting | 12 |  |  |  |  |  |  |
| 189 |  | 5 rock spur groynes | 200 |  |  |  |  |  |  |
| 190 |  | Rip rap - 15 lineal metres | 100 |  |  |  |  |  |  |
| 191 |  | Rip rap - 50 lineal metres | 300 |  |  |  |  |  |  |
| 192 |  | 4 Rock spur groynes | 120 |  |  |  |  |  |  |
|  |  | Top up 2 spurs - Arnold - September 2011 | 36 |  |  |  |  |  |  |
| 193 |  | Rip rap - 10 lineal metres | 50 |  |  |  |  |  |  |
|  |  | Added June 2009 - Arnold Contracting | 12 |  |  |  |  |  |  |
| 194 |  | Rip rap - 50 lineal metres | 400 |  |  |  |  |  |  |
| 195 |  | Spur groyne | 20 |  |  |  |  |  |  |
| 196 |  | Rip rap - 50 lineal metres | 364 |  |  |  |  |  |  |
| 197 |  | Rip rap - 25 lineal metres | 100 |  |  |  |  |  |  |
| 198 |  | 3 Rock spur groynes | 50 |  |  |  |  |  |  |
| 199 |  | Rip rap - 45 lineal metres | 300 |  |  |  |  |  |  |
|  |  | Added November 2004 | 96 |  |  |  |  |  |  |
| 200 |  | Rip rap - 20 lineal metres | 100 |  |  |  |  |  |  |
| 201 |  | Rip rap - 30 lineal metres | 150 |  |  |  |  |  |  |
|  |  | added 1997/98 | 100 |  |  |  |  |  |  |
| 202 |  | 5 rock spur groynes | 155 |  |  |  |  |  |  |
|  |  | Top up 2 spurs - Arnold - September 2011 | 39 |  |  |  |  |  |  |
| 203 |  | Rock spur groynes | 50 |  |  |  |  |  |  |
| 204 |  | 8 rock spur groynes | 300 |  |  |  |  |  |  |
|  |  | Added June 2009 - Arnold Contracting | 12 |  |  |  |  |  |  |
| 205 |  | 8 rock spur groynes | 275 |  |  |  |  |  |  |
|  |  | Added October 2002 | 80 |  |  |  |  |  |  |
| 206 |  | 5 rock spur groynes | 150 |  |  |  |  |  |  |
|  |  | added 1999/2000 | 60 |  |  |  |  |  |  |
|  |  | added January 2000 | 60 |  |  |  |  |  |  |
|  |  | Top up 3 spurs - Arnold - September 2011 | 185 |  |  |  |  |  |  |
| 206 | a | Place riprap between spurs - Arnold - September 2011 | 152 |  |  |  |  |  |  |
| 207 |  | Rock Weir | 300 |  |  |  |  |  |  |
| 208 |  | New riprap Twidle Added Feb 2011 Capital - Arnold | 1467 |  |  |  |  |  |  |
|  |  | Added April-May 2011 - Westland Contractors | 540 |  |  |  |  |  |  |
|  |  | Added April-May 2011 - Westland Contractors | 150 |  |  |  |  |  |  |
| 209 |  | New Stopbank - Twidle added April-May 2011 - West |  |  | 3900 |  |  |  |  |
| 210 |  | New Riprap - Twidle added April-May 2011 - West | 5022 |  |  |  |  |  |  |
| 211 |  | New stockpile at site of #61 | 86 |  |  |  |  |  |  |
|  |  | Summary | 271414 | 7499 | 610725 | 10000 | 1200 | 183440 | 23520 |
|  |  | Unit Rates | $ 30.00 | $ 29.00 | $ 7.50 | $ 1.00 | $ 30.00 | $ 1.50 | $ 3.50 |
|  |  | Calculated Costs | 8,142,420 | 217,471 | 4,580,438 | 10,000 | 36,000 | 275,160 | 82,320 |
|  |  | Total Estimated Assets as at 30 June 2014 | 13,343,808.50 |  |  |  |  |  |  |
|  |  | Add 10% Contingencies to cover Design etc | 1,334,380.85 |  |  |  |  |  |  |
|  |  | Add 2% for Resource Consent Costs | 293,563.79 |  |  |  |  |  |  |
|  |  | Total Including Contingencies | 14,971,753.14 |  |  |  |  |  |  |
|  |  | WORKS OUTSIDE SCHEME- CAPITAL |  |  |  |  |  |  |  |
| 49 | a | Riprap added 11.08 - Contract R 2008/11 - MBD | 970 |  |  |  |  |  |  |